## Slide 1
From Scripts to Systems
Day 1, From Script to Architecture
Python Application Architecture for Instrument Control
Notes: OPENING (2 min) Welcome delegates. Introduce yourself and the course theme. Set expectations: by end of Day 1, you'll understand why scripts break and have two powerful patterns (Adapter, Strategy) to fix that. Ice-breaker: 'Who here has a Python script that started small and grew into something terrifying?'

## Slide 2
About This Course
Who: engineers who write Python for instruments and want to write better software
What: build a working instrument-control application over 3 days
How: simulator-first, no real hardware required for any delegate
Every pattern appears first in simple form, then in a realistic context
Day 1: Architecture foundations | Day 2: GUI application | Day 3: Data and performance
Notes: COURSE OVERVIEW (3 min) Walk through each bullet. Emphasise 'simulator-first' so nobody worries about missing hardware. Ask: 'What instruments or devices do you work with day to day?' This helps you gauge the room. Mention the 3-day arc: foundations, application, data and performance.

## Slide 3
The Training Rig
SimulatedInstrument generates temperature and voltage readings
Accepts commands (READ:TEMP, SET:INTERVAL, *IDN?), returns realistic data
Can simulate errors: timeouts, garbage responses, intermittent disconnects, drift
Optional: one real Arduino/instrument rig on the instructor desk
All delegates work entirely with the simulator, no hardware dependency
Notes: SIMULATOR INTRO (3 min) Demo: run the simulator briefly in a terminal. Show it returning temperature and voltage values. Explain the commands: READ:TEMP, READ:VOLT, SET:INTERVAL:200, *IDN?, SET:ERROR_MODE:TIMEOUT. Key point: 'This simulator behaves exactly like a real instrument from your code\'s perspective.' Don't deep-dive the simulator yet. Students explore it in Lab 3.

## Slide 4
A Script That Works
200-line Python script: open serial port, read values, print them, write to CSV
It runs, it produces output, it does the job
For a one-off measurement task, this is absolutely fine
But what happens when the requirements change?
Notes: MOTIVATION (3 min) Show examples/messy_script.py on screen (or a snippet). Don't read through it line by line. Say: 'This works. For a one-off job, it\'s fine.' Pause. Then: 'So when does it stop being fine?' Validate that scripts aren't bad, they're just limited.

## Slide 5
A Script That Breaks
The boss wants a GUI
The instrument changes (new model, new protocol)
A second engineer has to maintain it
The data format needs to change (CSV to HDF5, add metadata)
Now add error handling, retries, timeouts...
Discussion: what has broken YOUR scripts?
Notes: DISCUSSION (5 min) Read each bullet, then STOP and ask: 'Has this happened to you?' Give 2-3 minutes for open discussion. Write keywords on whiteboard if available. This is the emotional hook: students should feel 'yes, this IS my problem' before you offer solutions.

## Slide 6
Why Scripts Break
Everything in one place, no separation of concerns
State scattered across global variables
Hardware details wired directly into application logic
No way to test without plugging in real hardware
One change ripples through the entire file
These are structural problems that patterns solve
Notes: ANALYSIS (3 min) Now formalise what they just described. Map their stories to these structural issues. Key misconception to address: 'My script is too small to need architecture.' Counter: 'It\'s not about size, it\'s about how many reasons it has to change.' Ask: 'If the serial port changes, how many lines do you edit?'

## Slide 7
The Goal — Architecture That Survives Change
Layered architecture: UI, Controller, Model, Adapter, Hardware/Simulator
Swap the instrument? Change one adapter file
Swap the data format? Change one sink file
Add a GUI? The model doesn't know or care
This is where we're heading over 3 days
Notes: ARCHITECTURE PREVIEW (3 min) Show the layered diagram. This is a preview, don't explain every layer yet. Say: 'By end of Day 3, your project will look like this.' Introduce the phrase casually: 'The controller does not care.' Don't over-explain. Students will build each layer themselves.

## Slide 8
OOP from Scratch
Classes, objects, state, and responsibility
Notes: SECTION TRANSITION (30 sec) 'Let\'s start building. We need objects before we can build patterns.' Gauge the room: 'How comfortable are you with Python classes? Show of hands.' Adjust depth based on the response.

## Slide 9
Functions vs Classes — When to Upgrade
Functions are great for stateless transformations: parse_reading(), format_timestamp()
Classes are for things with state and behaviour: a connection, a recorder, a sensor
Rule of thumb: if you pass the same 3 or 4 values between functions, you want an object
Don't oversell OOP, functions are fine when they're enough
Notes: CONCEPT (3 min) Stress the key distinction: functions for stateless transformations, classes for things with state. Ask: 'Would you pass port, baud_rate, and the serial handle to every function?' Common misconception: 'Classes are always better than functions.' Push back on this.

## Slide 10
Functions vs Classes — Code Example
Function (stateless)
Class (stateful)
def parse_reading(raw: str) -> float: """No state needed, just transform.""" parts = raw.strip().split(',') return float(parts[1]) result = parse_reading("TEMP,23.5,C")
class SerialConnection: """Has state: port, baud rate, open/closed.""" def __init__(self, port, baud_rate=9600): self.port = port self.baud_rate = baud_rate self._serial = None def open(self): self._serial = serial.Serial( self.port, self.baud_rate ) def read(self) -> str: return self._serial.readline().decode()
Functions for transformations, classes for things with state and identity
Notes: CODE WALKTHROUGH (4 min) Walk through both columns. Left: 'parse_reading takes a string, returns a float. No state needed. Perfect as a function.' Right: 'SerialConnection has a port, a baud rate, a serial handle. That\'s state. It belongs in a class.' Ask: 'What happens if you try to do the right-hand side with just functions?' This slide is the visual anchor for the concept. Point back to it during labs.

## Slide 11
What Is an Object
An object combines state, behaviour, and identity
Example: TemperatureReading has a value, a unit, a timestamp
Example: SerialConnection has a port, a baud rate, an open/closed state
Notes: CONCEPT (2 min) Keep this brief. The next slide has the code that makes it concrete. Avoid jargon like 'encapsulation', just say 'the data and the functions that work on it live together.'

## Slide 12
What Is an Object — Code Example
class TemperatureReading: """State: value, unit, timestamp. Behaviour: format, convert.""" def __init__(self, value: float, unit: str, timestamp: datetime): self.value = value self.unit = unit self.timestamp = timestamp def format(self) -> str: return f"{self.value:.2f} {self.unit}" def to_celsius(self) -> float: if self.unit == "F": return (self.value - 32) * 5 / 9 return self.value # Create an instance — a specific reading with its own identity reading = TemperatureReading(23.5, "C", datetime.now()) print(reading.format()) # "23.50 C"
Notes: CODE WALKTHROUGH (4 min) Live demo: type this class in the REPL or editor alongside the slide. Show: creating an instance, accessing attributes, calling methods. Ask: 'What\'s the difference between the class and an instance?' (blueprint vs actual thing) Point out the type hints, they document intent without heavy tooling.

## Slide 13
State and Responsibility
Every class should have one clear reason to exist
TemperatureSensor: reads temperature from the instrument
DataRecorder: writes readings to a file
If a class is doing two unrelated things, split it
Test: describe the class in one sentence. If you need "and", it's two classes
Notes: CONCEPT (3 min) This is the most important OOP idea in the course. Spend time here. Ask: 'Describe DataRecorder in one sentence.' If someone says 'It reads data AND writes it,' say: 'That\'s two things.' Key phrase: 'If you need AND to describe what it does, it\'s two classes.'

## Slide 14
State and Responsibility — Bad vs Good
Too many responsibilities
One job each
class InstrumentManager: """Reads AND records AND displays.""" def __init__(self, port): self.serial = serial.Serial(port) self.csv_file = open("data.csv", "w") self.label = QLabel() def do_everything(self): raw = self.serial.readline() value = float(raw.split(b",")[1]) self.csv_file.write(f"{value}\n") self.label.setText(f"{value:.2f}")
class Sensor: """Reads from instrument.""" def read(self) -> float: ... class Recorder: """Writes to file.""" def write(self, value: float): ... class Display: """Shows to user.""" def update(self, value: float): ... # Each can change independently
Notes: CODE WALKTHROUGH (5 min) Left column: 'InstrumentManager reads AND records AND displays. Three reasons to change.' Right column: 'Each class has one job. Sensor reads. Recorder writes. Display shows.' Ask: 'What happens if you need to change the display format?' Left: edit InstrumentManager (risky). Right: edit Display only (safe). This is the slide students will remember. Spend the time here.

## Slide 15
Composition vs Inheritance
Inheritance ("is a"): use sparingly, mainly for the adapter interface
Composition ("has a"): use by default, most instrument code benefits from this
DataAcquisitionSystem HAS a sensor, HAS a recorder, HAS a display
It is NOT a sensor, NOT a recorder, NOT a display
In instrument code, composition wins almost always
Notes: CONCEPT (3 min) In this course, inheritance appears once: the Adapter interface (ABC). Everything else is composition. Ask: 'Can anyone think of an is-a relationship in instrument code?' (Answer: rarely.)

## Slide 16
Composition vs Inheritance — Code
Inheritance (fragile)
Composition (flexible)
# Inheriting from the sensor? Really? class DataSystem(TemperatureSensor): """IS a sensor... but also records and displays?""" def record(self): ... def display(self): ... # What if we need two sensors? # What if we swap the sensor type? # Inheritance locks us in.
class DataSystem: """HAS a sensor, HAS a recorder.""" def __init__(self, sensor, recorder): self.sensor = sensor # injected self.recorder = recorder # injected def acquire(self): reading = self.sensor.read() self.recorder.write(reading) # Swap sensor? Pass a different one. # Add a second sensor? Add another field. # Composition keeps options open.
Notes: CODE WALKTHROUGH (4 min) Left: 'DataSystem IS a sensor? That makes no sense. What if we need two sensors?' Right: 'DataSystem HAS a sensor, HAS a recorder. Swap either one independently.' Key insight: 'Composition keeps options open. Inheritance locks you in.'

## Slide 17
How to Slice Logic into Small Units
Find the nouns: instrument, reading, recorder, config, display
Find the verbs: connect, read, record, display, configure
Assign each verb to the right noun
If a noun has too many verbs, split it into two nouns
Notes: PRACTICAL METHOD (3 min) Do this exercise live with the class. 'What are the nouns? What are the verbs? Now assign each verb to the right noun.' This is a design heuristic, not a formal method.

## Slide 18
Lab 1 — From Script to Classes
You will receive a messy 200-line script (examples/messy_script.py)
Read through it and identify at least 3 distinct responsibilities
Create a class for each responsibility
Refactor main() so it creates instances and calls methods, no globals
The refactored version should produce the same output
Time: 25 to 30 minutes
Notes: LAB SETUP (2 min then 25-30 min lab) Point students to examples/messy_script.py. Say: 'Don\'t try to make it perfect. Just find 3 responsibilities and give each one a class.' Walk the room. Common issues: students who freeze (suggest nouns), too many classes, where main() goes.

## Slide 19
Lab 1 Debrief
What classes did you create?
Good answers: InstrumentReader, DataRecorder, ReadingFormatter
Common mistake: creating classes that are just namespaces (no state)
Common mistake: making one giant class that does everything
There's no single right answer, but some splits are clearly better
Notes: DEBRIEF (5 min) Ask 2-3 students to share their class names. Write them on the board. Common good answers: InstrumentReader, DataRecorder, ReadingFormatter. Bridge to afternoon: 'Now let\'s look at real instrument code and find the patterns.'

## Slide 20
Patterns in Instrument Programming
Seams, adapters, and strategies
Notes: SECTION TRANSITION (30 sec) Post-lunch is low energy. Start with the messy driver demo. Say: 'We\'re going to look at some truly awful code.'

## Slide 21
The Messy Driver
150-line instrument driver (examples/messy_driver.py)
Mixed concerns: serial setup, command formatting, response parsing, error handling
Hardcoded port, baud rate, command strings
It works, but changing anything is risky
Notes: DEMO (5 min) Show examples/messy_driver.py on screen. Scroll through slowly. Point out: hardcoded port, serial setup mixed with formatting, scattered error handling. Ask: 'Where would you start cleaning this up?'

## Slide 22
What Is a Seam
A seam is a point where you can change behaviour without editing surrounding code
In instrument code, seams are at: the transport layer, the command format, the response parser, and the error handler
The seams tell you where to cut
Notes: CONCEPT (3 min) Define seam: 'A point where you can change behaviour without editing surrounding code.' Analogy: 'Like a seam in clothing.' List the four seams. Ask students to identify which seam each problem belongs to.

## Slide 23
Finding Seams — Code Example
def read_temperature(self): # SEAM 1: Transport — hardcoded serial setup ser = serial.Serial('/dev/ttyUSB0', 9600) # SEAM 2: Protocol — hardcoded command format ser.write(b'READ:TEMP\n') # SEAM 3: Parsing — coupled to response format response = ser.readline().decode() value = float(response.split(',')[1]) # SEAM 4: Error handling — scattered if value < -50 or value > 150: print("WARNING: suspect reading") return value
Four seams in one function. Each is a reason to change. Each should be its own concern.
Notes: CODE WALKTHROUGH (5 min) Walk through each SEAM annotation. SEAM 1: hardcoded serial. SEAM 2: hardcoded command. SEAM 3: parsing coupled to format. SEAM 4: scattered error handling. Ask: 'If I change the instrument model, which seams do I cut?' (Potentially all, which is the problem.) This is the key teaching slide for seams.

## Slide 24
Refactoring Toward Clarity
Before: everything tangled
After: seams separated
def read_temperature(self): ser = serial.Serial('/dev/ttyUSB0', 9600) ser.write(b'READ:TEMP\n') raw = ser.readline().decode() value = float(raw.split(',')[1]) return value
def read_temperature(self): raw = self.transport.send('READ:TEMP') return self.parser.extract_value(raw) # Transport is injectable (real or fake) # Parser is a pure function (testable) # read_temperature() just orchestrates
Notes: CODE WALKTHROUGH (4 min) Left: 'Everything tangled. Hardcoded port, inline command, inline parsing.' Right: 'Transport is injectable. Parser is pure. read_temperature() just orchestrates.' Say: 'I didn\'t change what the code does. I changed how it\'s organised.'

## Slide 25
Lab 2 — Refactor the Messy Driver
Receive the messy driver (examples/messy_driver.py)
Identify the seams (transitions between concerns)
Extract at least the transport layer and parsing logic
Goal: the driver should be testable without a real serial port
Keep the FakeSerial class unchanged, it simulates the port
Time: 30 minutes
Notes: LAB SETUP (2 min then 30 min lab) Key instruction: 'Keep the FakeSerial class unchanged.' This lab is harder than Lab 1. Allow full 30 minutes. If students struggle, pair them up.

## Slide 26
Lab 2 Debrief
Key insight: separating transport from protocol makes everything testable
The Transport class can accept any serial-like object (real or fake)
Pure parsing functions can be tested with simple string inputs
This separation is the foundation for the Adapter pattern, up next
Notes: DEBRIEF (5 min) Key insight: 'Separating transport from protocol makes everything testable.' Bridge: 'What you just did informally has a name. It\'s called the Adapter pattern.'

## Slide 27
Code Married to Hardware
serial.Serial('/dev/ttyUSB0', 9600) appears in 47 places
Change the instrument? Rewrite everything
Test without hardware? Impossible
One serial timeout crashes the entire GUI
If your code can only run when the hardware is plugged in, your code owns you
Notes: MOTIVATION (3 min) Pause after: 'If your code can only run when the hardware is plugged in, your code owns you.' Ask: 'Who has code that can only be tested with the real instrument?' Say: 'By the end of this session, that will never be true again.'

## Slide 28
The Adapter Pattern
Define an interface (the port): connect(), read_value(), send_command(), disconnect()
Implement it twice: RealInstrumentAdapter and SimulatedInstrumentAdapter
The rest of your code talks only to the interface, never to serial.Serial directly
This is the single most important pattern in the course
Notes: CORE CONCEPT (4 min) This is the single most important slide in the course. Draw the diagram: Application -> InstrumentAdapter (interface) -> Real OR Simulated. Key phrase: 'The controller does not care whether the instrument is real or simulated.'

## Slide 29
The Adapter Interface — ABC
from abc import ABC, abstractmethod class InstrumentAdapter(ABC): """The contract. Any instrument must implement these.""" @abstractmethod def connect(self) -> None: ... @abstractmethod def disconnect(self) -> None: ... @abstractmethod def read_value(self, channel: str) -> 'Reading': ... @abstractmethod def send_command(self, command: str) -> str: ... @property @abstractmethod def is_connected(self) -> bool: ...
Five methods. That's the entire contract. Any class implementing these can be used as an instrument.
Notes: CODE WALKTHROUGH (5 min) Walk through each method of the ABC. Ask: 'Why does read_value() take a channel parameter?' (Multiple channels.) Ask: 'Why is is_connected a property?' (State, not action.) This is the contract everything else depends on.

## Slide 30
Simulated vs Real Adapter
SimulatedInstrumentAdapter
RealInstrumentAdapter
class SimulatedInstrumentAdapter(InstrumentAdapter): def connect(self): self._connected = True # instant def read_value(self, channel): # Sine wave + noise, no hardware t = time.time() value = 22 + 3 * math.sin(t / 10) value += random.gauss(0, 0.1) return Reading(value, "degC", channel) def disconnect(self): self._connected = False
class RealInstrumentAdapter(InstrumentAdapter): def connect(self): self._serial = serial.Serial( self._port, self._baud_rate ) def read_value(self, channel): self._serial.write( f"READ:{channel}\n".encode() ) raw = self._serial.readline().decode() return self._parse(raw) def disconnect(self): self._serial.close()
Same interface, completely different internals. The calling code cannot tell the difference.
Notes: CODE WALKTHROUGH (5 min) Walk both columns. Left: simulator. Right: real hardware. Same interface. Bottom note: 'The calling code cannot tell the difference.' If you have a demo rig, this is the moment to show the same script on both.

## Slide 31
Swapping at Startup
def create_adapter(config: dict) -> InstrumentAdapter: """Factory: config chooses the adapter, app doesn't care.""" device_type = config['device']['type'] if device_type == 'simulated': return SimulatedInstrumentAdapter() elif device_type == 'serial': return RealInstrumentAdapter( port=config['device']['port'], baud_rate=config['device']['baud_rate'] ) else: raise ValueError(f"Unknown device type: {device_type}") # In main.py — ONE line decides real vs simulated adapter = create_adapter(config) # Everything below this line is identical # regardless of which adapter was created adapter.connect() reading = adapter.read_value("temperature")
Notes: CODE WALKTHROUGH (4 min) Show the factory function. 'ONE line decides real vs simulated.' Key point: 'Architecture makes the swap possible. Configuration makes it easy.' Preview: on Day 3, this comes from a YAML file.

## Slide 32
Lab 3 — Build the Adapter
Review the InstrumentAdapter ABC in labmonitor/core/adapter_interface.py
Review SimulatedInstrumentAdapter in labmonitor/drivers/simulated.py
Write a test script that creates the adapter, connects, reads 10 values, disconnects
Verify: isinstance(adapter, InstrumentAdapter) is True
Extension: try toggling error modes
Time: 30 minutes
Notes: LAB SETUP (2 min then 30 min lab) Students work with the labmonitor project for the first time. Key instruction: 'Use the adapter through the interface only.' Extension: try toggling error modes.

## Slide 33
Lab 3 Debrief
Demo: same script, two different adapters, identical calling code
The key insight: the calling code does not know or care which adapter is behind it
"The controller does not care."
This phrase is the architectural mantra of the entire course
Notes: DEBRIEF (4 min) Demo: same script, two adapters, identical code. Say the mantra: 'The controller does not care.' Ask: 'To add a third adapter for a network instrument?' (One new class. Nothing else changes.)

## Slide 34
The Problem — Measurement Modes
Your instrument supports: single reading, continuous, burst, averaging
Without the Strategy pattern: massive if/elif chain
Adding a new mode means editing the core logic, risky and ugly
Every time you see a big if/elif for different modes, you're looking at a Strategy opportunity
Notes: MOTIVATION (3 min) Show the concept of the big if/elif chain. Ask: 'What happens when the boss asks for a new mode?' Same structural problem as hardcoded hardware, but for behaviour.

## Slide 35
The Strategy Pattern — Bad vs Good
if/elif sprawl
Strategy objects
def measure(self, mode, adapter): if mode == 'single': return [adapter.read_value('temp')] elif mode == 'continuous': results = [] for _ in range(self.n_readings): results.append( adapter.read_value('temp') ) time.sleep(self.interval) return results elif mode == 'averaging': values = [adapter.read_value('temp') for _ in range(self.n_samples)] avg = sum(v.value for v in values) avg /= len(values) return [Reading(avg, 'degC', 'temp')] # Adding a new mode? Edit here. # Hope nothing breaks.
class MeasurementStrategy(ABC): @abstractmethod def execute(self, adapter) -> list: ... class SingleRead(MeasurementStrategy): def execute(self, adapter): return [adapter.read_value('temp')] class Averaging(MeasurementStrategy): def execute(self, adapter): vals = [adapter.read_value('temp') for _ in range(self.n)] avg = sum(v.value for v in vals) avg /= len(vals) return [Reading(avg, 'degC', 'temp')] # Adding a new mode? New class. Done.
Notes: CODE WALKTHROUGH (5 min) Left: 'if/elif sprawl. Adding a mode means editing core logic.' Right: 'Strategy objects. Each mode is its own class.' Ask: 'How many files change for BurstReadStrategy?' (One new file.) Draw the parallel to Adapter.

## Slide 36
Combining Adapter + Strategy
# The controller picks a strategy and an adapter. # Neither knows the other's internals. adapter = create_adapter(config) # could be real or simulated strategy = create_strategy(config) # could be single, continuous, averaging adapter.connect() readings = strategy.execute(adapter) # strategy uses adapter adapter.disconnect() # New device? New adapter class. Strategy unchanged. # New mode? New strategy class. Adapter unchanged. # M strategies x N adapters, all interchangeable.
Notes: CODE WALKTHROUGH (4 min) This is the synthesis slide. 'Controller picks strategy and adapter. Neither knows the other\'s internals.' M strategies x N adapters, all interchangeable.

## Slide 37
Lab 4 — Implement Strategies
Review the strategy implementations in labmonitor/core/strategies.py
Write a script that creates all three strategies
Run each strategy on the same SimulatedInstrumentAdapter
Show that strategies are interchangeable: write a run_strategy() function
Extension: create a BurstReadStrategy or FilteredStrategy
Time: 20 minutes
Notes: LAB SETUP (2 min then 20 min lab) Shorter lab. Pattern should feel familiar. Key instruction: 'Write a run_strategy() that takes ANY strategy and ANY adapter.' Extension: create a BurstReadStrategy.

## Slide 38
Day 1 Recap
Started with a messy script, identified why it breaks
Learned OOP: objects, state, responsibility, composition
Identified seams in a messy driver and refactored toward clarity
Built an Adapter to abstract hardware (real vs simulated)
Built Strategies to abstract measurement behaviour
Tomorrow: wrap all of this in a real PySide6 desktop application
Notes: CLOSING (5 min) Recap: messy script, objects, seams, Adapter, Strategy. Ask each table to name one thing they learned. Preview tomorrow: 'We wrap it all in a PySide6 desktop application.' End on time.